## Slide 1: Vibration Measurement in Astronomical Observatories
Jonathan Zerez
Olin College of Engineering
Mentors:
Hugh Thompson, Lianqi Wang, Peter Byrnes
Organization:
Thirty Meter Telescope

## Slide 2: Extremely Large Telescopes
Basics of TMT:
TMT is massive
TMT’s Goal: Understand more about the universe
In order to achieve these goals:
Design parts that meet optical performance requirements
Notes:   30 meter diameter mirror, world’s current largest is 10 meters
  Answer key questions about the structure and evolution of the universe
  Explore the enigmatic processes, environments and bodies that encompass the universe.
  Vibrations are the limiting factor of ground based telescopes. Trying to keep 70nm wavelength aberrations over a 30 meter area. 10^6.5

## Slide 3: Vibrations are bad for Image Quality
Have many potential sources
Can’t always be eliminated
Point source without vibrations
Point source with vibrations
Notes: Sources: Earthquakes, Wind, Elevation/Azimuth acutators, pumps, fans, cooling lines, bearings, etc
Vibration budget: systems engineering tool used to assign vibration requirements to components based on vibrational sensitiviy analysis. Lots of assumptions based on finite element modeling, needs validation with physical testing data. Garbage in, garbage out.

## Slide 4: The Vibration Budget
Define allowable levels of vibration
Finite Element Models used
Physical testing
& data acquisition
Analytical results
Vibration Budget
FEA
Assumptions
Validation

## Slide 5: FEMs need Validation
Transfer Functions
Vibrational Sources
Will current plans/components for the telescope meet requirements set out by the vibration budget?
Notes: Vibration budget: systems engineering tool used to assign vibration requirements to components based on vibrational sensitiviy analysis. Lots of assumptions based on finite element modeling, needs validation with physical testing data. Garbage in, garbage out.

## Slide 6: Project Overview
Physical testing
& data acquisition
Analytical results
Vibration Budget
FEA
Assumptions
Validation

## Slide 7: Project Overview
Physical testing
& data acquisition
Analytical results
Vibration Budget
FEA
Assumptions
Validation

## Slide 8: Data Acquisition Tools & Validation
MATLAB
-User Interface
-Data Processing
National Instruments
-Data Acquisition
ANSYS
-Simulation and modeling

## Slide 9
Specify collection settings
Impact Detection
Data processing, plotting, and averaging
Saving and loading data
Labview mode!

## Slide 10: Testing Methodology
Impact Hammer (B&K 8207)
Accelerometer 1 (PCB Triaxial)
Article
Accelerometer 2 (PCB Triaxial)
1
2
Notes: How was testing carried out?
-Used an instrumented impact hammer
-Used Accelerometer to read impulse response of the MSIT close to the impact location
-Used second accelerometer to read impulse response of MSIT far from impact locaiton and determine transfer function

## Slide 11: Validating the tools
Ensure tools are processing data correctly on simple systems
Legitimize tool’s utility for more complex systems

## Slide 12
Impact Hammer
1
2
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 13
Impact Hammer
1
2
Even Frequency Distribution
Frequency Roll-off
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 14
Accelerometer 1
1
2
Modes of pendulum cables
Rigid Body Frequencies
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 15
Article
1
2
Inverse Mass Line (known)
Inverse Mass Line (calculated)
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 16: Additional Insights Generated from the Tool

## Slide 17
Accelerometer 1
1
2
Poor coherence at low and high frequencies
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 18
Article
1
2
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 19
Accelerometer 2
1
2
Low Frequency Amplification
Fundamental Frequency
Notes: Impact hammer used to carry out testing
-Puts an short impulse into the structure
-Covers wide range of frequencies
-Low signal to noise ratio, need to average multiple hits
-Notice timescale of time domain plot

## Slide 20: MSIT Background and Testing Rationale
The Multi-Segment Integration and Test (MSIT) structure
MSIT Ansys Finite Element Model (Static Structural)
Notes: -This is the MSIT, it will be used to hold a series of 7 fixed frames and mirror segments for the purposes of testing and integration
-Lives in the monrovia lab
-Used in testing because:
-Has a corresponding CAD/FEM to extract analytical estimations to compare physical data
-Have easy access to physical structure
-Similar to the M1 support structure

## Slide 23: Summary
Developed and validated vibrational testing tool
Vibrational data acquired from the MSIT
Need to extract simulated characteristics of the MSIT to compare to real life data

## Slide 24: Takeaways
Acquisition tools allow for efficient modal testing for engineers
Starting to close the loop of design

## Slide 25: Acknowledgements
Hugh Thompson; TMT
Peter Byrnes; TMT
Lianqi Wang; TMT
Gelys Trancho; TMT
Jamie Nakatawase; TMT
Thirty Meter Telescope International Observatory
Akamai Internship Program
  Institute for Scientist & Engineer Educators at UCSC
  Funding
    Thirty Meter Telescope International Observatory
    Air Force Office of Scientific Research (FA9550-15-1-0427)
    Hawaii Community Foundation Career Connected Learning Program
    Daniel K. Inouye Solar Telescope
    W. M. Keck Observatory (via NSF AST-1836016)
    University of Hawaii at Hilo
    Canada-France-Hawaii Telescope
Bryan Smith; TMT
Fred Kamphues; TMT
Chris Carter; TMT
Amir Sadjadpour; TMT
Doug MacMartin; Cornel